## Slide 1: CHE 670 Sustainability Seminar
GHG Calculators
David A. Carter
Kansas State University Pollution Prevention Institute
January 6, 2010

## Slide 2
``I think you should be more explicit here in step two...''

## Slide 3: EPA Greenhouse Gas Equivalencies Calculator
Uses the Emissions & Generation Resource Integrated Database (eGRID) U.S. annual non-baseload CO2 output emission rate
Puts carbon dioxide (CO2) emissions reductions in everyday terms
May be useful in communicating your greenhouse gas reduction strategy, reduction targets, or other initiatives aimed at reducing greenhouse gas emissions
Useful for emissions reductions from energy efficiency or renewable energy programs
Only for CO2, no other GHG
http://www.epa.gov/RDEE/energy-resources/calculator.html

## Slide 4: EPA’s Pollution Prevention GHG Calculator
Quantifies reductions based on conversion factors
  Electricity conservation
  Green energy
  Fuel substitution
  Greening chemistry
  Water conservation
  Materials management
GHG Conversion Tool_May 2009.xls

## Slide 5: EPA’s Mandatory Reporting Rule
Tier 1: CO2 = 1x10-3 x Fuel x HHV x EF
  Fuel = mass or volume of fuel combusted/year (mass in short tons, volume in scf [gas] or gallons [liquid]
  HHV = default high heat value (Table C-1) (mmBTU/mass or volume)
  EF = fuel-specific default CO2 emission factor
  1x10-3 = conversion factor for kg to metric tons

## Slide 6: EPA’s Mandatory Reporting Rule
Tier 2: CO2 = 1x10-3 x Fuel x HHV x EF
  HHV = annual average high heat value of fuel from all valid samples for the year
    If fuel samples > monthly, HHV (annual) = ∑ (HHV)i x (Fuel)i
    ∑(Fuel)i
Tier 3: depends on solid, liquid, gas
Tier 4: CEMS

## Slide 7: EPA Applicability Tool
Assess whether your facility would be required to report GHG
Applicability depends on the source categories and, for some source categories, the emission level or production capacity
Not intended for Suppliers of fossil fuels or industrial GHGs and Engine Manufacturers
Applicability Tool

## Slide 8: The Climate Registry
General Reporting Protocol, May 2008
Electric Power Sector Protocol
Oil and Gas Production Protocol
Local Government Operations Protocol (adopted June 2, 2009)
Data Quality Tiers
  A1 Direct Monitoring
  A2 Calculation based on fuel use (measured carbon content and measured heat content)
  B Calculation based on fuel use (measured heat content and default carbon content, or vice versa)
  C Calculation based on fuel use (default CO2 emission factors by fuel type)

## Slide 9: The Climate Registry
Estimating emissions from stationary combustion using fuel use data involves six steps
  Determine annual consumption of each fuel combusted at your facility
  Determine the appropriate CO2 emissions factors for each fuel
  Determine the appropriate CH4 and N2O emissions factors for each fuel
  Calculate each fuel’s CO2 emissions
  Calculate each fuel’s CH4 and N2O emissions, and
  Convert CH4 and N2O emissions to CO2 equivalent and determine total emissions

## Slide 10: EPA Climate Leaders Simplified GHG Emissions Calculator (SGEC)
Based on Climate Leaders GHG protocol guidance
Determines direct and indirect emissions at all sources in the company
http://www.epa.gov/climateleaders/documents/sgec_tool_v2%208.xls

## Slide 11: GHG Protocol
Default emission factors are averages based on the most extensive data sets available
Largely identical to those used by the Intergovernmental Panel on Climate Change (IPCC)
Businesses should use custom values whenever possible
Cross-sector tools
  Stationary combustion
  Purchased electricity, heat, and steam
  Transport or mobile sources
  Employee commuting
  Refrigeration and air-conditioning
http://www.ghgprotocol.org/calculation-tools/all-tools
  Stationary combustion tool

## Slide 12: American College & University Presidents Climate Commitment (ACUPCC)
Clean Air-Cool Planet Campus Carbon Calculator: http://www.cleanair-coolplanet.org/toolkit/content/view/43/124/

## Slide 13: Comparison of Calculators
57,200,000 scf natural gas
GHG Equivalencies – 2,860 metric tons CO2e (therms)
P2 GHG Calculator – 3,128 (scf); 3,043 (therms)
Climate Leaders – 3,131 (scf)
EPA Applicability Tool – 3,118 (scf)
GHG Protocol – 3,053 (scf); 3,386 (therms)
ACUPCC – 3,017,628 (MMBTU)